## Slide 1: Simulation and Modeling
CSE4131_CSE4132

## Slide 2: Few examples…
Reference Book:
  System Simulation with Digital Computer
  By- N. Deo
Chapter No.: 1 (Introduction)

## Slide 3: Classifications

## Slide 4: An other Example
Simulation of a Chemical Reactor
  Its an example of a continuous system
  Its an example of dynamic system
  Question may come:

## Slide 5
Problem statement (2013) (2011)
In a chemical reactor:
  There are two substances: A & B
  A + B = third chemical substance C
  Its known:
    1 gram of A + 1 gram of B  produces 2 grams of C
  The rate of formation of C is:
    proportional to presence of A & B
  Backward reaction - decomposition of C back in to A & B:
    The rate of decomposition proportional to the amount of C present in the reactor

## Slide 6: Simulation of a Chemical Reactor
Let a, b & c … are quantities of A, B & C at any time t
  Then their rate of increases are described by the following three differential equation.

## Slide 7: Simulation of a Chemical Reactor
Given the values of the
  constants k1 and k2 and
  the initial quantities of the chemicals A and B (and C = 0),
we wish to determine how much of C has been produced as a function of time.
  Determination of the rate of such chemical reactions is important in many industrial processes
A straightforward method of simulating this system is to start at time zero and
  increment time in small steps of ∆t.

## Slide 8
A
B
C = 0
δt

## Slide 9: Simulation of a Chemical Reactor
    We assume that the quantities of chemicals remain unaltered during each step and only change 'instantaneously' at the end of the step.
    Thus the quantity of A (or B or C) at the end of one such step is given in terms of the quantity at the beginning of the step as
Identical equitation can be written for b(t+∆t) and c(t+∆t)

## Slide 10: Simulation of a Chemical Reactor
Suppose we want to do the simulation for a period T
  We will divide T into a large number N of small periods ∆t
  That is,
At the time zero, we know a(0), b(0) and c(0)
We also know k1 & k2

## Slide 11: Simulation of a Chemical Reactor
From these values we compute the amount of chemical at the time ∆t :

## Slide 12
Using the steps we calculate 3∆t, 4∆t … N∆t  T

## Slide 14: Sample output